## Slide 1: Thesis Advisory Committee Meeting -1
Pravein Govindan Kannan
Advisor : Prof. Chan Mun Choon
Notes: Hello Everyone.
Thanks for attending the thesis advisory committee.
So, let me introduce myself formally, I am Pravein, I am entering the 4th year of my PhD

## Slide 2: Agenda
Raptor: Rule Placement in SDN (~10 min)
BNV: Bare metal network virtualization (~30 min)
Ongoing/Future Work (~10 min)
Notes: Let me lay out the agenda for this presentation :
Initially, I will be giving a 10-min quick run through of my first work, Raptor which is a scalable rule placement scheme in Software defined networks.
Next, I will be talking about the work I was doing last year, which is BNV, a bare-metal network virtualization technique
Finally, I will conclude with the work

## Slide 3
Raptor: Scalable Rule Placement over Multiple Path in Software Defined Networks
IFIP Networking 2017
Notes: Let me go into Raptor, a scalable rule placement scheme for multi-path/dynamic traffic in software defined networks.

## Slide 4: Software Defined Networking
Forwarding
Forwarding
Forwarding
Forwarding
SDN Controller
App1
App2
App n
Network Policies
Access Control (ACL)
Traffic Measurement
Rate Limiting
Traffic Engineering
OpenFlow
Raptor
Notes: In Software Defined Networking, Switches implement forwarding, and controller configures the entire network by implementing Network policies.
Benefit of this being, the controller gets a complete view of the network, and can operate network policies considering the entire network as a single switch.
Network policies could typically be :
Access control, which limits the communication for certain traffic.
Traffic measurements.
Rate limiting on the traffic throughput
And certain types of traffic engineering.

## Slide 5: Network Policies translation to Switches
MAC SRC
MAC DST
IP SRC
IP DST
TCP Dport
TCP SPort
VLAN ID
...
ACTION
Rule Matching
PRIORITY
Raptor
Action
Notes: The network policies are implemented by rules in the switches, which match on the headers and take the corresponding actions.
For any incoming packet to a switch, it has to be matched with all the rules, and takes the action of it’s corresponding matched rule.

## Slide 6: Network Policies to Switches
Where is the Flow tables (rules) Stored?
TCAM
Power-Hungry (~60%)
Expensive
Few thousand Entries (1K-10K)
Increasing demands for individual policies(per-flow)
Rule placement is crucial to scale!!
Raptor
Notes: These rules are stored in a high speed look-up memory knows as TCAM(Ternany content addressable memory)
which does the entire search operation in a single lookup,
However, it is very expensive, power hungry, and limited to few thousand entries in the switches.
And, with increasing demands for per-flow policies in virtualized data-centers,
rule placement is very crucial in-order to support the increasing demands.

## Slide 7: Rule Placement Scenarios
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
Match
Raptor
Notes: Let me illustrate rule placement by example.
Let’s consider the following 4 rules to be placed on the network with 4 hosts H1,H2, H3 and H4, connected by the underlying network.
Basically, the rules have the match criterion as the source and destination IP, and the port number optionally and finally the action to be taken for that match.

## Slide 8: Placement of Rules at Ingress
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
Raptor
Notes: Lets, consider the default placement implemented by SDN Controllers, where rules are placed on the ingress of the network, where it applies to.

## Slide 9: Placement of Rules at Ingress
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
1
Raptor
Notes: Looking at Rule 1: since it applies to traffic between H1 and H3, It is placed in Switch S1, which is the ingress switch for this particular traffic.

## Slide 10: Placement of Rules at Ingress
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
1
2
Raptor
Notes: Consider Rule 2, which applied between H2, and H3/H4. Hence, this rule will be placed in Switch S2, which is ingress switch of this packet path.

## Slide 11: Placement of Rules at Ingress
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
1
2
3
3
3
3
Raptor
Notes: Consider Rule 3, which applies to traffic originating from all hosts towards H4. Hence, this rule is applied to all the ingress switches S1, S2, S6 and S7

## Slide 12: Placement of Rules at Ingress
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
1
2
3
3
3
4
4
3
4
Total Rules Needed = 10
Problem :
No. of Rules limited to Capacity of Ingress switches.
4
Raptor
Notes: And Rule 4 similarly, applies to traffic between all pairs of hosts. Hence., needs to be placed in all ingress switches.
Hence, after placing all the rules/policies. Overall number of rules needed to implement the policies is 10.
This is the most simple rule-placement scheme, however
The Problem is that number of rules is limited to capacity of ingress switches, which could be limited and in the order of few thousands.

## Slide 13: Existing works on Rule Placement
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
VCRIB [NSDI 13], PALETTE [INFOCOM 13], OBS [CoNext 13]
Raptor
Notes: To solve this scalability problem, there are a range of works which perform placement of rules by splitting and offloading the rules along the path of traffic.

## Slide 14: Existing works on Rule Placement
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
1
2
3
3
3
4
4
4
4
VCRIB [NSDI 13], PALETTE [INFOCOM 13], OBS [CoNext 13]
Address Scalability problem  Offload Rules along the path
Raptor

## Slide 15: Existing works on Rule Placement
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
1
2
3
3
3
4
4
4
4
VCRIB [NSDI 13], PALETTE [INFOCOM 13], OBS [CoNext 13]
Address Scalability problem  Offload Rules along the path
Raptor

## Slide 16: Existing works on Rule Placement
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
1
2
3
3
3
4
4
4
4
VCRIB [NSDI 13], PALETTE [INFOCOM 13], OBS [CoNext 13]
Address Scalability problem  Offload Rules along the path
Raptor

## Slide 17: Existing works on Rule Placement
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
1
2
3
3
3
4
4
4
4
VCRIB [NSDI 13], PALETTE [INFOCOM 13], OBS [CoNext 13]
Address Scalability problem  Offload Rules along the path
Total Rules Needed >= 10
Problem :
Flows restricted to Single Path :
  Dynamic Load Balancing
  Path Failures.
Raptor
Notes: Hence, now the rules are split to avoid any conflicts, and offloaded onto the path of the applicable traffic.
The total number of rules in the network will be greater than 10, due to conflict resolution, which causes rules to be splitted and hence increases the number of rules needed.
The problems of these schemes are that,
The rules are placed considering the single path for a flow; Hence, upon path failures, it needs to re-calculate and place the rules in the alternative path. Same goes for load-balancing dynamically.
Hence, its not very practical for networks with dynamic flows and traffic engineering.

## Slide 18: Existing works on Rule Placement
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
1
2
3
3
3
4
4
4
4
PALETTE [INFOCOM 13], OBS [CoNext 13] , VCRIB[NSDI 13]
Address Scalability problem  Offload Rules along the path
Total Rules Needed >= 10
Problem :
Flows restricted to Single Path :
  Dynamic Load Balancing
  Path Failures.
Naïve Duplication of rules in multi-path is not scalable!! Can we do Better?
Raptor
Notes: We can consider naïve duplication of rules to support multipath, however again, its not very scalable. Can we do better?

## Slide 19: Raptor
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
1
2
3
3
3
3
4
4
4
4
Key Idea : Rule Sharing !!
Shareable Rules
Raptor
Notes: In Raptor, the key idea is to identify rules that are applicable to various flows, and placing them at certain points in network, where it can be shared.
For example, rule 3 and 4 are applicable to more than 1 host pair, hence, can be moved to a more central part of the network, without much changes.

## Slide 20: Raptor
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
1
2
3
3
3
3
4
4
4
4
Key Idea : Rule Sharing !!
Shareable Rules
Raptor

## Slide 21: Raptor
ID | Source | Destination | Action
1 | H1(00) and tcp-port:80 | H3(10) and tcp-port:80 | Drop
2 | H2(01) | H3,H4(1*) and tcp-port:443 | Drop
3 | All(*) | H4(11) | Counter
4 | All(*) | All(*) and tcp-port :22 | Drop
3
3
3
4
4
S6
S3
S1
S2
S7
S4
H1 (00)
H2 (01)
H3 (10)
H4 (11)
S5
1
2
3
4
4
Key Idea : Rule Sharing !!
Key Techniques :
Offload Rules to switches considering rule sharing.
Place rules considering multi-path.
Total Rules Needed = 5
Shared Rules
Raptor
Notes: By doing this, rule 3 and 4 are now placed Switch S5 , we just need 1 rule for implementing rule 3 and 2 rules for implementing rule 4 (since S5 doesn’t hit the traffic between H1 and H2).
Also, the position of S5 here is perfect since regardless of the path the traffic takes, it will hit the rule.
Hence, the number of rules needed in the network reduce by half in this small example itself.

## Slide 22: Raptor Overview
SDN Controller
Connect
Rule Placement
Endpoint Policy
Topology & Paths
Diffuse
Formulate the problem as an Integer Linear Program to get a partial solution.
Solve the Integer Linear Program without ordering constraint.
Raptor
Notes: The First phase, diffuse, we solve the ILP without ordering constraint to get a partial solution.

## Slide 23
Raptor Overview
SDN Controller
Rule Placement
Endpoint Policy
Topology & Paths
Diffuse
Connect
Re-arrange the rules to maintain ordering
Raptor
Notes: Let me now go into the solution,
Given the Topology(with the selected paths) and the endpoint policy.
We go through two phases.

## Slide 24: Evaluation – for Fat-Tree
Fat-Tree-8 – More Overlap
Fat-Tree-8 – Less Overlap
Save 40-100% over OBS-1;
80-140% over OBS-2
Scales 3X over Ingress
1.75X over OBS
Raptor
Notes: In FatTree-8, we observe savings of 40-60% over OBS-1 for less overlapping policies.
Adding to that, we observe that we are able to accommodate larger policy-set for a given topology and switch tcam size.

## Slide 25
BNV : Enabling High-Fidelity Experimentation
through Bare-metal Network Virtualization

## Slide 26: How to validate Innovative Ideas?
Optimizing Topologies
Congestion Control
Bandwidth Allocation
CONDOR [SIGCOMM 15] : No Single Topology is optimal for all use cases
Forwarding
Forwarding
Forwarding
Forwarding
SDN Controller
App1
App2
App n
OpenFlow
Notes: New paradigms and architectures such as SDN have added an unprecedented increase n the rate of Research & Development conducted in the field of computer networks.
Be it Looking out for new topologies for data-centers, designing congestion control protocols or bandwidth allocation, There is a need to validate the new ideas in an environment which can guarantee high-fidelity and provide flexibility.

## Slide 27: Can a Staging environment reliably mimic production?
Notes: In Big Environments, small configuration issues could bring down the network causing large outages.
To minimize the outages, the configuration changes could be tried out in staging environment which can reliably mimic production at scale.

## Slide 28: Software Tools : Flexible
Mininet, Maxinet: Elegant tools enabling functional testing/ learning.
Container-based virtualization on a single machine or cluster of machines.
Cannot achieve the peak line-rate performance testing.
Notes: In many cases, experiments rely on software network emulation tools like mininet, maxinet gns3 etc.
These tools allow experimenters to create network topologies very quickly on the host machines using container-based techniques
However, since they run on the CPU of the machines they are hosted on, the network performance highly depends on the deployment environment.
Also, they cannot achieve peak line-rate for performance testing

## Slide 29: Network Testbeds – High Fidelity
DeterLab, CloudLab, GENI, Staging Platforms:
Can provide high fidelity emulation with Bare-Metal provisioning.
Can provide only a fixed topology or subset for programmable networks.
Change in Topology are in the order of days to months for wiring changes.
Notes: Network testbeds such as cloudlab, deterlab and other platforms provide high-fidelity environment for network experimentation.
However, they consider the network as an infrastructure rather than tools to be experimented with.
Though some testbeds like GENI provide network that are programmable, they can only provide a fixed topology or a subset of the substrate topology.
In order to get fexilbility/ change in topology it would take in the order of days to months for wiring changes

## Slide 30: How do we achieve the flexibility of software and fidelity of hardware?
Topology Scaling : one-to-many switch virtualization
Notes: So, How do we achieve the flexibility of software tools, and fidelity of hardware based testbeds?
The answer is topology scaling, i.e. to virtualize a single switch to many virtual switches in an arbitrary fashion

## Slide 31: Topology Scaling (one-to-many virtualization)
CoVisor [NSDI 2015]
256; inport = 1,dstip = 2.0.0.0/16; fwd(2)
112; inport = 1,dstip = 1.0.0.0/24; fwd(3)
76; inport = 1,dstip = 1.0.0.0/8; dstip = 2.0.0.0, fwd(4)
Symbolic Path Generation
Priority Augmentation
4 o 0 o 0
1 o 6 o 0
1 o 1 o 4
Notes: CoVisor performs one-to-many virtualization of a switch using policy composition.
In this example, A single switch S is virtualized into 3 different switches logically.
Now, assume the 3 switches have 2 rules in each of them for forwarding.
So, what CoVisor does is analyzes the rules in each switch, and combines the rules when applying to the physical switch in such a way that the correctness is right, in terms of priority.

## Slide 32: Topology Scaling (one-to-many virtualization)
CoVisor [NSDI 2015] : Doesn’t capture Queuing behavior
S1
H1
H2
S2
H3
H4
1G
1G
1G
1G
1G
Ping
iperf
S1
H1
H2
H3
H4
1G
1G
1G
1G
Ping
iperf
Notes: However, Since, it manipulates the policies to emulate multiple switches, it doesn’t capture the queuing behavior between the switches.
So, to demonstrate that, we have a experiment with 4 hosts,
Initially, we have 4 hosts, and 2 switches, the links are 1G each, we run continuous ping from h1 to h4, from 30th to 60th second, we run iperf between H2 and H3, sharing the same bottleneck link.
So, what we observe happens to the ping’s RTT is shown in the green dashed lines, since the iperf traffic fills the queues, thus increasing the latency of the ping traffic.
So, with covisor composing policies, we cannot observe the queing behavior since it switches in the backplane, and there is no
link

## Slide 33
Virtual Topology
Switch1
Switch2
Switch3
Network Hypervisor
OpenFlow
Tenant 2
ONOS Controller
Tenant 1
OpenDaylight Controller
Tenant Mapping
Tenant 3
POX Controller
FatTree, JellyFish, HyperCube, HyperX, Xpander, Arbitrary topologies…etc
Tenant n
…
Any SDN Controller
Notes: So, what we ideally need is a network hypervisor, which can take the substrate switches, and the users’s topologies, and allow users’s to control their network from there on.
Regardless of the topologies.

## Slide 34
Virtual Topology
Switch1
Switch2
Switch3
BNV
OpenFlow
Flow Translation
Topology Abstraction
Tenant 2
ONOS Controller
Tenant 1
OpenDaylight Controller
BNV Mapper
Tenant Mapping
Tenant 3
POX Controller
FatTree, JellyFish, HyperCube, HyperX, Xpander, Arbitrary topologies…etc
Tenant n
…
Any SDN Controller
Notes: So, BNV is the network hypervisor, which connects the switches using OpenFlow.

## Slide 35
Flow Translation
Topology Abstraction
Notes: Lets look at how topology is abstracted to make 3 switches to many arbitrarily connected switches.

## Slide 36: GENERIC Topology
5
5
1
2
3
4
1
2
3
4
H1
H2
H3
H4
H5
H6
H7
H8
pSwitch1
pSwitch2
CLink1
10G
Notes: Lets see a generic topology with 2 switches, and 8 hosts. The hosts are connected to the switch using 1G links and 10G backhaul links.

## Slide 37
5
5
1
2
3
4
1
2
3
4
H1
H2
H3
H4
H5
H6
H7
H8
pSwitch1
pSwitch2
CLink1
V1
V3
1
2
3
2
3
1
V2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
vL1
vL2
vL3
1G
1G
1G
10G
Notes: Now, if we want to embed a virtual topology with 3 switches to this infrastructure, The mapping will be done as follows.

## Slide 38
5
5
1
2
3
4
1
2
3
4
H1
H2
H3
H4
H5
H6
H7
H8
pSwitch1
pSwitch2
V1
V3
1
2
3
2
3
1
V2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
CLink1
vL1
vL2
vL2
1G
1G
1G
10G

## Slide 39
5
5
1
2
3
4
1
2
3
4
H1
H2
H3
H4
H5
H6
H7
H8
pSwitch1
pSwitch2
V1
V3
1
2
3
2
3
1
V2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
CLink1
vL1 -> CLink1
vL2
vL3
1G
1G
1G
10G

## Slide 40
5
5
1
2
3
4
1
2
3
4
H1
H2
H3
H4
H5
H6
H7
H8
pSwitch1
pSwitch2
V1
V3
1
2
3
2
3
1
V2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
CLink1
vL1 -> CLink1
vL2
vL3
1G
1G
1G
10G

## Slide 41
5
1
2
3
4
1
2
3
4
H1
H2
H3
H4
H5
H6
H7
H8
pSwitch1
pSwitch2
V1
V3
1
2
3
2
3
1
V2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
CLink1
vL1 -> CLink1
vL2 -> CLink1
vL3
1G
1G
1G
10G
5

## Slide 42
1
2
3
4
1
2
3
4
H1
H2
H3
H4
H5
H6
H7
H8
pSwitch1
pSwitch2
V1
V3
1
2
3
2
3
1
V2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
CLink1
vL1 -> CLink1
vL2 -> CLink1
vL3 -> Bounce Link
1G
1G
1G
10G
5
5
Final Mapping

## Slide 43
5
5
1
2
3
4
1
2
3
4
H1
H2
H3
H4
H5
H6
H7
H8
pSwitch1
pSwitch2
CLink1
V1
V3
1
2
3
2
3
1
Tag 3
vL1 : Tag 1
Tag 2
V2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
Link 1 using Packet Tagging
PKT
PKT
PKT
1
PKT

## Slide 44
5
5
1
2
3
4
1
2
3
4
H1
H2
H3
H4
H5
H6
H7
H8
pSwitch1
pSwitch2
CLink1
V1
V3
1
2
3
2
3
1
Tag 3
vL1: Tag 1
vL2: Tag 2
V2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
Link 2
PKT
PKT
2
PKT
PKT

## Slide 45
5
5
1
2
3
4
1
2
3
4
H1
H2
H3
H4
H5
H6
H7
H8
pSwitch1
pSwitch2
CLink1
V1
V3
1
2
3
2
3
1
vL3: Tag 3
vL1: Tag 1
V2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
Link3 :
Bounce back Link
PKT
PKT
PKT
3
PKT
vL2: Tag 2
Core link Overhead

## Slide 46
X
NH
NL/2
NL/4
Y
Always
Feasible
Feasibility depends on topology
X: Number of Hosts Y: Number of inter-switch links
H Ports
H Ports
Core Network
……
N Switches
Capacity L
Capacity L
Size of Virtual network
Notes: In order to gauge the size of a network that could be virtualized using this approach. Consider N switches having H ports connected to host, and backhail link of capacity L. Consider the host links are of capacity 1 unit.
In the best case, upto NL/2 switch-to-switch links can be supported.. In the worst case, the mapping places all switch-pairs with connected links in the same physical switch thus, using up more core-capacity.
Hence, NL/4 switch-to-switch links can be supported.

## Slide 47: Can we do better?

## Slide 48: Idea : Loopback links in substrate topology

## Slide 49: Idea : Loopback links in substrate topology

## Slide 50: Idea : Loopback links in substrate topology

## Slide 51: Topology + Loopback link
5
5
1
2
3
4
1
2
3
4
H1
H2
H5
H6
pSwitch1
pSwitch2
CLink1
LoopLink1
LoopLink2

## Slide 52
5
1
2
3
4
1
2
3
4
H1
H2
H5
H6
pSwitch1
pSwitch2
CLink1
V1
V3
1
2
3
2
3
1
vL1 -> CLink1
vL2 -> CLink1
V2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
LoopLink1
LoopLink2
5

## Slide 53
5
1
2
3
4
1
2
3
4
H1
H2
H5
H6
pSwitch1
pSwitch2
CLink1
V1
V3
1
2
3
2
3
1
vL1 -> CLink1
vL2 -> CLink1
V2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
LoopLink1
LoopLink2
5
vL3 -> LoopLink1
Notes: Now, with loopback links, the mapping vL3 can be mapped to the looplink1 instead of the CLink1

## Slide 54
5
5
1
2
3
4
1
2
3
4
H1
H2
H5
H6
pSwitch1
pSwitch2
CLink1
H1
H5
1
2
3
2
3
1
vL3: Tag 3
VL1 : Tag 1
H2
2
3
1
vS1
vS2
vS3
Physical Topology
Virtual Topology
Link3 :
Loop Link
PKT
PKT
vL2: Tag 2
LoopLink1
LoopLink2
1) Consistency & Fidelity of mapping.
2) No Traffic Overhead in Core Link.
Notes: Now, advantages are that :
1) This mapping resermbles an actual switch to switch link
2) It causes no overhead on the core link.

## Slide 55: Topology Scaling (one-to-many virtualization)
S1
H1
H2
S2
H3
H4
1G
1G
1G
1G
1G
Ping
S1
H1
H2
H3
H4
1G
1G
1G
1G
iperf
Notes: Taking a look at the initial experiment to see how loopbacks compare to two physically connected switches, we repeat the same experiment with an experiment containing loopback link to emulate two connected switches.

## Slide 56
Always
Feasible
Feasibility depends on topology
X: Number of Hosts Y: Number of inter-switch links
H Ports
H Ports
Core Network
……
N Switches
Capacity L
Capacity L
X
Y
NL/4
NL/2
NL/4+NH/2
NL/2+NH/2
Gain using loopback links
In Always feasible region.
NH
Size of Virtual network
How do we decide how many
loopback links
per switch?
Notes: Checking the size of the network that can be emulated using loopback links.
The H ports of the switches can either connect to a host or be a loopback link.

## Slide 57: Software-Configurable Loopbacks
Notes: Additionally, we can also make loopback entirely dynamic and software configurable if we can interconnect the servers and the SDN switch using an L2 switch,
Then, we can manipulate VLANs to create loopbacks or connect servers as the demand arises.

## Slide 58
Virtual Topology
Switch1
Switch2
Switch3
BNV
OpenFlow
Flow Translation
Topology Abstraction
Tenant 2
ONOS Controller
Tenant 1
OpenDaylight Controller
BNV Mapper
Tenant Mapping
Tenant 3
POX Controller
FatTree, JellyFish, HyperCube, HyperX, Xpander, Arbitrary topologies…etc
Tenant n
…
Any SDN Controller

## Slide 59
Virtual Topology
Switch1
Switch2
Switch3
BNV
OpenFlow
Flow Translation
Topology Abstraction
Tenant 2
ONOS Controller
Tenant 1
OpenDaylight Controller
BNV Mapper
Tenant Mapping
Tenant 3
POX Controller
FatTree, JellyFish, HyperCube, HyperX, Xpander, Arbitrary topologies…etc
Tenant n
…
Any SDN Controller

## Slide 60
BNV Mapper
Notes: Lets look at how the network embedding is done using BNV Mapper

## Slide 61: BNV Mapper (Virtual Network Embedder)
1
1
BNV
Mapper
Request
Mapping
1
1
1
1
10

## Slide 62: BNV Mapper
A Virtual Topology Consists of :
  A set of hosts V,
  A set of (virtual) switches S,
  A set of (virtual) links L
H1
H3
H5
H7
H2
H4
H6
H8
Host Link
Core Link

## Slide 63: BNV Mapper
Solved using ILP
Variables :
Core Link::
Host link:
Notes: BNV Mapper is basically an ILP formulation with variables for core link and host link.

## Slide 64: BNV Mapper
Objective is to Minimize the usage of Core-links:
a) Maximizes isolation to the tenant, keeping links dedicated.
b) Provides scope for dynamic expansions. (Adding/upgrading tenants)
Inter-Switch
Links
Big-Switch abstraction
Notes: The objective of the formulation is to minimize the usage of core links,
1) Why we do this is to maximize the isolation to the tenant, by giving dedicated links when possible.
2) Additionally, it provides scope for expansions using core links by providing locality to the embedding.

## Slide 65: BNV Mapper - Constraints
1) Core Link one-to-one mapping:
2) Host Link one-to-one mapping:
3) Host Link Bandwidth constraint:
4) TCAM capacity constraint
Notes: So, the constraints are core links mapping, host link mapping, host link bandwidth constraint and TCAM capacity constraint so that we do not allocate beyond the capacity of the switch.

## Slide 66: BNV Mapper - Constraints
5) One Big Switch Abstraction:
Total Bandwidth of mapped to n
Matrix for each : Indicates intra-switch bandwidth to be allocated between two physical switches
Notes: So, with the mapper, recall that we can either map a single switch into many switches and the other way, i.e. many switches into a single switch.
When we map many switches into a single switch, we need to account for the backplane bandwidth to be allocated between the switch port.
So, this constraint takes care of that. Let me explain using an example.

## Slide 67: BNV Mapper – Big Switch Abstraction
CLink1
Core Network
1
2
3
H1
H2
H3
pSwitch1
1
2
3
H4
H5
H6
pSwitch2
1
2
3
H7
H8
H9
pSwitch3
CLink2
CLink3
vSwitch1
H1
H2
H3
H4
H8
Physical Topology
Virtual Topology
To | B/W
H4 | 1G
H7+H8 | 2G
To | B/W
* | 1G
To | B/W
H1+H2+H3 | 2G
H4 | 1G
H7
Notes: Consider a vswitch1 with hosts allocated using servers across 3 different switches
Pswitch1 has 3 hosts, pswitch2 has 1 host and pswitch3 has 2 hosts allocated from substrate to constitute vswitch1.
So, using bnvmapper, we identify the maximum bandwidth to be allocated for the core link between the switches.
For example, the core link1 needs 3G provisioned since that maximum traffic that can be received by the other hosts is 3.
However since corelink 2 can only generate/ receive 1G traffic, we ratelimit the traffic to that. So going back to the formulation..

## Slide 68: BNV Mapper - Constraints
5) One Big Switch Abstraction:
Total Bandwidth of mapped to n
Matrix for each : Indicates intra-switch bandwidth to be allocated between two physical switches
Notes: So, This constraint calculates the bandwidth between each physical switch which belongs to a same virtual switch, and allocates the minimum between a pair of phy switches.

## Slide 69: BNV Mapper - Constraints
6) Core Link Bandwidth constraint:
Inter-Switch
Links
Intra-Switch
fabric
Notes: Finally, the core link bandwidth constraint which accounts both the inter-switch and intra-switch bandwidth.

## Slide 70: BNV Mapper – Topology Convertibility
Re-run the ILP with the modified objective
To maximize using the same switch-ports/links
Notes: Additionally, tenants may need to change their topology dynamically. So to do that, we rerun the ILP with a modified objective to maximize the usage of the same ports/ links allocated to the topology.

## Slide 71: Implementation
Implemented on top of
Integrated with a Bare-metal provisioning service (Testbed).
Deployed on NCL Production Environment.
Notes: We implemented BNV on top of OpenVirteX, which is an existing network hypervisor. Additionally integrated with a bare-metal provisioning service deterlab.
It is currently deployed on NCL production environment for experimenters to spawn SDN based experiments with arbitrary topologies.

## Slide 72: Implementation
Support OpenFlow 1.0/ 1.3
MAC address encodes <Tenant-id, Link-Id>
Rate-limiting using Switches’ classifier based QoS.
Notes: Our implementation supports OpenFlow 1.0 & 1.3.
We implement the link tagging by encoding it in Mac address when a packet enters the network and by removing the tag when it leaves the network.
The rate-limiting is implemented in the switches using classifier based QoS which overrides OpenFlow.

## Slide 73: Implementation
Dynamic Loopback Wiring
using L2 intermediate Switch
Static loopback wiring
24-ports of SDN Switch
Notes: The implementation platform over 4 clusters of 24 blades is shown in the figure. We use 12 loopbacks per SDN switch. Thus enabling 12 switch-to-switch links within the same switch.
We have also testbed dynamic loopback wiring in a staging setup.

## Slide 74: Evaluation
Can BNV faithfully replicate behaviour of topologies?
Provide control/data plane isolation to multiple tenants?
Scale of complex topologies embedded?
Notes: To evaluate BNV, we seek answers to 3 questions :
Can bnv faithfully replicate the behavior of topologies.
Can we provide control/ dataplane isolation to multiple tenants/ experimenters?
How big topologies can be embedded using BNV?

## Slide 75: Evaluation : loopbacks & Big Switch Abstraction
Notes: Lets answer the first question using application behavior:
We emulate star topology with multiple switches in our topology using the big switch abstraction.
And we emulate clos topology with a single switch in BNV using loopbacks

## Slide 76: Evaluation : loopbacks & Big Switch Abstraction

## Slide 77: Evaluation : loopbacks & Big Switch Abstraction
Star (Single Switch)
Star (Multi Switch)
Clos (Multi Switch)
Clos (Single Switch)
Notes: We run a wordcount application on apache spark for a large amount of data (50GB) and plot the CDF of the shuffle read completion times.
Note that the intended topology on the left is the actual topology’s behavior
We observe that either the topology is emulated using a single switch or multiple switches, it has the same behavior in terms of the shuffle read times of the spark.

## Slide 78: Mapping Complex Topologies
Notes: So, in this illustration we show how we can map a fat-tree topology with degree 4 on BNV’s substrate topology with just 2 switches.
Each pod links are emulated using the loopbacks, and the core links are used to inter-connect pods.

## Slide 79: Evaluation : Fidelity of Complex Topologies
Single-Rooted Tree
Fat Tree
Jellyfish
Star
Notes: In This experiment, we embed 4 topologies on BNV, to observe the application behavior on each of the virtual topology which have same no. of hosts, but the network topology different.
We run Hadoop and apache spark. We display the results of apache spark

## Slide 80: Evaluation : Fidelity of Complex Topologies
Single-Rooted Tree
Fat Tree
Jellyfish
Star
Single-Rooted Tree
Single-Rooted Tree
Single-Rooted Tree
Single-Rooted Tree
Single-Rooted Tree
Single-Rooted Tree
Single-Rooted Tree
Single-Rooted Tree
Single-Rooted Tree
Single-Rooted Tree
Single-Rooted Tree
Single-Rooted Tree
Fat Tree
Fat Tree
Fat Tree
Fat Tree
Fat Tree
Fat Tree
Fat Tree
Fat Tree
Fat Tree
Fat Tree
Fat Tree
Fat Tree
Jellyfish
Jellyfish
Jellyfish
Jellyfish
Jellyfish
Jellyfish
Jellyfish
Jellyfish
Jellyfish
Jellyfish
Jellyfish
Jellyfish
Star
Star
Star
Star
Star
Star
Star
Star
Star
Star
Star
Star

## Slide 81: Evaluation : Fidelity of Complex Topologies
Single-Rooted Tree
Fat Tree
Jellyfish
Star
Notes: As expected Tree has the highest shuffle time due to restricted b/w, and star has the lowest time due to the highest bandwidth

## Slide 82: Evaluation : Fidelity of Complex Topologies
Single-Rooted Tree
Fat Tree
Jellyfish
Star

## Slide 83: Evaluation : Fidelity of Complex Topologies
Fat Tree
Jellyfish
28.02
26.32
Jellyfish
7-8% Lower
Low Intra-pod locality
Heavy cross rack traffic!!
Notes: Now lets focus on two topologies FatTree and jellyfish.
Jellyfish performs better than fatree (about 7-8% better). We observe this behavior because the traffic pattern of the application was low intra-pod locality, and there was heavy cross traffic, due to partitions and broadcasts.

## Slide 84: Evaluation : Fidelity of Complex Topologies
Fat Tree
Jellyfish
19.06
17.647
High Intra-pod locality
Low cross rack traffic!!
Jellyfish
8% Higher
Take-away: BNV emulates the intrinsic characteristics of the topologies, otherwise observed with heavy wiring & building costs
This observation is backed by Tale of Two Topologies [SIGCOMM ’17]
Notes: Now, we change the Application’s traffic pattern to create more intra-pod locality and thus low cross rack traffic.
With this change, we observe reduce in shuffle read times. However, more important observation is that now jellyfish observes higher shuffle time than fat-tree.
This observation is same as that observed by a recent paper on convertible topologies using a fully wired network.
Thus, the take-away is that BNV emulates the intrinsic characteristics of topologies, without the need for wiring changes and building costs.

## Slide 85: Evaluation : Isolation of multiple tenants
Fat Tree
Jellyfish
Random (Rest of the nodes)
Take-away: BNV can support multiple arbitrary tenants providing isolated & repeatable environments.
Notes: Next, we evaluate BNV’s ability to achieve traffic isolation between multiple experiments/tenants.
So, we spawn three experiments : Fatree running the spark application, jellyfish running iperf between all nodes, and a random topology formed using the rest of the nodes, and capturing ping between the network.
Initially, we run each of the experiment separately, to capture the performance without any other experiment running.
From 60th minute to 80th minute, all 3 expts are running in parallel, we observe that, each expts do not affect each other regardless of its running separately or combined.
So, we can achieve isolated and repeatable enironments using BNV

## Slide 86: Evaluation : Scale of Topologies
Notes: The last set of experiments is a simulation to see how much.
So, the topology we consider is with 5 tor sdn switch, connected to 24 servers and 12 loopbacks each.
The backhaul network is 40Gs

## Slide 87: Evaluation : Scale of Topologies
Notes: We run our experiments consider with and without loopbacks in the network. And plot the percentage of core bandwidth used.
Without loopbacks, we can implement only upto degree 4 of fattree
But with loopback we can go upto degree 6 (with upto 212 links) using the given substrate,

## Slide 88: Evaluation : Scale of Topologies
Notes: Next, we map variations of random topologies, with n switches, and links either as n sqrtn or 2n links.
With loopbacks we observe 2X gain in the scale of topologies that can be supported. Without loopbacks, we tend to do poor also due to use of bounce links which cause additional overhead on the core link.

## Slide 89: Evaluation : Scale of Topologies
Take-away: Addition of loopback links increases the scalability significantly.
Can emulate topologies with 130 switches and 300 links with just 5 ToR switches
Internet Topology Zoo dataset
Notes: Finally, we embed the topologies from topology zoo dataset, and we see with loops we could support upto topologies of 300 links, which covers about 95% of the topologies from the dataset,
Final takeaway is that we can emulate large topologies as much as 130 switches and 300 links with just 5 switches, and still maintaining the fidelity of the emulation.

## Slide 90: Summary
BNV provides High-fidelity network experimentation/cloud platform.
BNV can scale a network to support arbitrary topologies using the existing network.
Can emulate networks of more than 100 network devices with just 5 ToR Switches.
Implemented in NCL testbed for over six months for experimentation.
In Submission to SOSR 2018.
Notes: So, to summarize
BNV can be used to provide an high-fidelity network experimentation platform.
We have implemented BNV in NCL bare-metal based testbed for over six months for experimentation.

## Slide 91: Ongoing Work
Support Virtualization for Programmable Data-Plane P4:
Use-Cases:
Composable data-plane for modularity.
Different tenants running completely independent protocols.
A/B Testing of data-plane protocols.
Network upgrades and snapshots.
Notes: Next, I am working on enabling virtualization of data-plane in P4.
So, the purpose of doing that would be to :
Achieve modularity while programming data-plane ( using parallel and sequencial operations of various basic p4 programs), so that its easier for operators to enable/disable features.
Enabling multiple tenants program their own set of data-plane functionalities sharing the same infrastructure
Enabling A/B testing of protocols by releasing only to a select few.
Easing network upgrades and snapshotting.

## Slide 92: Ongoing Work
Approach :
Compose multiple programs using compile-time analysis and re-factoring.
Merge Parsers, Ingress Table, Egress Tables
Identify Tenant/
Program
Notes: The approach I have taken is by composing multiple programs using compile time analysis and re-factoring of the tables and parsers.

## Slide 93
P4 Runtime Hypervisor
Data Path 1
Protobuf
Data Path 2
Data Path 3
Meta

Push BNV header
BNV header =>
BNV header =>
Pop BNV header
Notes: After refactoring, lets assume the topology, the bnvp4 would need to integrate with p4 runtime, to identify the topology, and combine p4 programs at the edge using the meta-data.
At the edge, the p4 program would add a BNV header (16-bit tenant-id), and at the egress edge, it will pop the header and forward.
Currently, I can combine multiple p4 programs to make s super p4 program of them.
I am in progress of integrating with p4 runtime to implement the end-to-end solution. Once I do that, I want to see the performance

## Slide 94
Thank You

## Slide 95: Backup

## Slide 96: Related Work
Network Hypervisors
FlowVisor[OSDI ’10] VeRTIGO[EWSDN ’12] OpenVirteX[HotSDN ’14]
Switch Abstractions
VINI[SIGCOMM ’06] Trellis[CoNEXT ’08] Mininet[CoNEXT ’12] MaxiNet[Networking ’14]
MiniReal[ICC ’17] CrystalNet[SOSP ’17]